## Slide 1: Romana Networks
Cloud Native SDN

## Slide 2
Leaf 1
Spine splits full 10/8 CIDR across 4 Leaf devices (four /10 networks)
Leaf allocates /10 network across 64 ports assigning a /16 address block to each
  Host on Leaf 1, Port 8 must get address within 10.7.0.0/16
  Host on Leaf 4, Port 3 must get address within 10.194.0.0/16
0.0.0.0 via Spine 1
10.0.0.0/16 via Port 1
10.1.0.0/16 via Port 2
10.2.0.0/16 via Port 3
10.3.0.0/16 via Port 4
…
10.63.0.0/16 via Port 64
Spine 1
0.0.0.0 via Internet
10.0.0.0/10 via Leaf 1
10.64.0.0/10 via Leaf 2
10.128.0.0/10 via Leaf 3
10.192.0.0/10 via Leaf 4
Spine 2
Leaf 2
Leaf 3
Leaf 4
0.0.0.0 via Internet
10.0.0.0/10 via Leaf 1
10.64.0.0/10 via Leaf 2
10.128.0.0/10 via Leaf 3
10.192.0.0/10 via Leaf 4
0.0.0.0 via Leaf 1
Port 8
Host
10.194.3.71
0.0.0.0 via Leaf 4
Port 3
Host 8
10.7.16.34
0.0.0.0 via Spine 1
10.192.0.0/16 via Port 1
10.193.0.0/16 via Port 2
10.194.0.0/16 via Port 3
10.195.0.0/16 via Port 4
…
10.255.0.0/16 via Port 64

## Slide 3
Leaf gets full /10 network and allocates /16 to each Host
Host allocates /24 to up to 255 VMs
For Containers on VM get IP out of VM’s /24
Host 7
VM 1
VM 2
VM 255
R7
10.6.255.1/24
Kubernetes Pod IP: 10.6.1.18
Host 8
VM 1
VM 2
VM 255
R8
10.7.255.1/24
Host 9
VM 1
VM 2
VM 255
R9
10.7.1.1/24
10.6.1.1/24
10.8.1.1/24
10.8.255.1/24
0.0.0.0 via Spine 1
10.6.0.0/16 via Port 7
10.7.0.0/16 via Port 8
10.8.0.0/16 via Port 9
Spine 1
0.0.0.0 via Internet
10.0.0.0/10 via Leaf 1
0.0.0.0 via Leaf 1
G/W: 10.6.0.1/16
0.0.0.0 via Leaf 1
G/W: 10.7.0.1/16
0.0.0.0 via Leaf 1
G/W: 10.8.0.1/16
Leaf 1
Romana
Host Agent

## Slide 4: North/South Traffic
Latency dramatically reduced
  No Network node
  No encap
Identical path for East/West traffic
Eliminated
Bypassed
Bypassed
Romana Router
Romana Router
1 Top of Rack Round Trip
Per Network Security

## Slide 5
GW
S1
D1
F1
Local Net
S2
192.168.0.10
10.1/16
10.1.1.2
10.2.1.3
10.1.2.2
10.1.0.1
10.1.0.1
10.1.0.1
10.2.0.1
10.1.1.129
Endpoint
Default Gateway IPs
Endpoint IPs
GW
S1
D1
F1
S2
192.168.0.10
10.1.1.2
10.2.1.3
10.1.2.2
10.1.1.129
10.1.0.1
10.1.0.1
10.2.0.1
10.1.1.129
Endpoint
Default Gateway IPs
Endpoint IPs
10.1.0.1
Local Net
Local Net
Local Net
10.2/16
10.2.0.1
10.1/16
10.1.0.1
10.2/16
10.2.0.1

## Slide 6
Neutron plugin
Romana
Managers
Auth
IPAM
Topology
Routes
Tenant
Root
Storage
RDBMS
Key/Value store
CLI
Go
client
library
Python
client
library
Hypervisor Hosts
Romana agent
Romana agent
Romana agent
Romana Agent

## Slide 7: Single Host L3 Service Insertion
Host 1
Insert Service Function F1
  Change S1 GW to F1 IP
  SF IP has /25 ‘service bit’ set
S1 sends traffic to D1
  S1 forwards to F1
  F1 forwards to GW
  GW forwards to D1
Works across Segments on same host
S1 sends traffic to D2
  S1 forwards to F1
  F1 forwards to GW
  GW forwards to D2
GW
S1
D1
F1
IP Tables Rules
S2
D2
192.168.0.10
10.1.0.1/16
10.1.1.2
10.1.1.3
10.1.2.2
10.1.2.3
10.1.1.129
10.1.1.1
10.1.1.1
10.1.1.1
10.1.1.1
10.1.1.129
Endpoint
Default Gateway IPs
Endpoint IPs
Key Point: Manipulating GW preserves destination IP in header

## Slide 9: Route Aggregation
R Leaf 1
Leaf gets full /9 network and allocates /16 to each Host
Romana IPAM assigns each Host an IP from /16
For Containers on Host, Host is allocated its own /24
Containers on VM get IP out of VM’s /24
Node 1
VM1
VM2
VM3
VM4
R1
A1
B1
A2
C1
10.1.4.1/24
A1 POD IP: 10.1.1.18
Node 2
VM1
VM2
VM3
VM4
R2
C2
B2
A3
C3
10.2.4.1/24
Node 3
VM1
VM2
VM3
VM4
R3
DNS
LB
FW
NAT
10.2.1.1/24
10.1.1.1/24
10.3.1.1/24
10.3.4.1/24
0.0.0.0 via Spine
10.1.0.0/16 via Node 1
10.2.0.0/16 via Node 2
10.3.0.0/16 via Node 3
R Spine
0.0.0.0 via Internet
10.0.0.0/9 via Leaf 1
10.128.0.0/9 via Leaf 2
0.0.0.0 via Leaf 1
G/W: 10.1.0.1/16
0.0.0.0 via Leaf 1
G/W: 10.2.0.1/16
0.0.0.0 via Leaf 1
G/W: 10.3.0.1/16
Simple example
  8 Host bits
  8 Segment bits

## Slide 10: L3 Tenancy Model
Tenant ID in IP address
  IPv6 Preferred Deployment
  IPv4 for Small/Typical Deployment Today
Contains tenant ID of source and destination
  ACLs verified at both ends
  Easily enforced by host at source or destination
Enables massive route aggregation
  Static routing in physical infrastructure
  Updating routes on host becomes familiar distributed app configuration management
Requirements:
  Fully routed infrastructure
  Intelligent IP address management (IPAM)
  Route distribution
  Integration with CMS (i.e. OpenStack, Kubernetes, etc.)
IPv6 Address
Prefix: Net Space/Location
IID: Host/Tenant ID
FF-FE
Phys Host ID
Tenant, Segment, IID
EUI-48 Expansion
RFC 1918 IPv4 Addresses
10/8 Offers Ample Room
0010
Segment
Host ID

## Slide 11: Routed VXLANs
Neutron Network node routes traffic between segments
Network node performs all L3 functions
East/West traffic encapsulated, but forwarded directly to destination host
VXLAN Decap
VXLAN Encap
VXLAN Decap
VXLAN Encap
Per Instance
Security
2 Top of Rack
Round Trips
In-Segment East/West
Traffic

## Slide 12: Kubernetes Pods Inside Instance
Host 2
Host 1
Host 2
Host 1
VLAN (good)
or
VXLAN (2nd encap)
Eliminated
Eliminated
2nd Encap
VLAN (good)
or
VXLAN (2nd encap?)
Instance 1
Instance 2
Encap
Instance 1
Instance 2
Tap Interface G/W to Pod IPs
Eliminated
Romana Router
Romana Router

## Slide 13
North/South Latency reduced 50%-85%
10% improvement for East/West traffic between hosts (no encap)
No performance penalty for local on-host East/West traffic
 | North/South (Routed) |  | East/West (Switched) | 
Time (ms) | Local | Remote | Local | Remote
Native OpenStack | 1.51* | 1.51 | 0.24 | 0.85
Romana Networks | 0.24 | 0.77 | 0.24** | 0.77**
Relative Performance | Local | Remote | Local | Remote
Native OpenStack | 100% | 100% | 100% | 100%
Romana Networks | 16% | 51% | 100% | 90%
* All N/S OpenStack traffic
goes off host
** All Romana traffic is routed